## Slide 1: Alien P.R.O.B.E RFID Reader/Scanner App
.
Cy Dixon, Nicholas Johnson, Alex Godsey, Michael Lynch
Western Kentucky University/WKU Parking and Transportation/Computer Science Department
This project is a team effort done in conjunction with the WKU Parking and Transportation Services for our team’s CS 496 Senior Project course.
This app, Alien P.R.O.B.E., was created in order to offer PTS employees a simple app for use in their daily tasks. This app connects to the Alien ALR-F800 RFID Reader along with the Alien ALR-8689 RFID Antenna, both pictured to the right.
WKU Parking and Transportation Services plan to use this app to scan a vehicles’ RFID parking tag, and then determine if that tag is on the correct vehicle and in the correct parking lot based on the GPS location. This is all done within the app, through its connection with databases and the RFID equipment.
  Requirements
The Alien P.R.O.B.E. app is developed for Android devices with Android OS 11.0 and later, as this meets the requirements of the phones provided to the parking enforcement employees at WKU Parking and Transportation Services.
  The app requires a connection to the RFID Reader through either the network or through Bluetooth. This allows the app to retrieve the tags the RFID Reader picks up and decodes.
  The app has a small hardware usage and only takes up 26.9 MB of storage space so it should be able to be easily installed on all or most phones that PTS provides their employees.
Pictured above is the Alien RFID ALR-F800 Reader and below it is the Alien ALR-8698 RFID Ultra-band Antenna.
The RFID Antenna broadcasts radio frequency (RF) signal, the passive RFID tags stored in the parking tags receive this energy and become activated. These tags utilize the energy from the RF signals to send back their own signals, which contain the information stored in the tags' microchips.
The RFID Reader receives these signals through the antenna. It then processes and decodes the information encoded within the signal.
Once decoded, the information gathered from the tags can be sent to our Alien P.R.O.B.E. app via network or Bluetooth connection. The application stores this data and sends the information to a database along with the phone’s current GPS location. The database verifies if the permissions that belong to that RFID tag give authority to park in the current location. If unauthorized, the application alerts the user of the invalid parking.
The app also maintains an internal database of the scanned tags for the user to view later, storing the tag info, the GPS coordinates when the tag was scanned, as well as the time when the tag was scanned. Thi allows the user to have a reference to determine the validity of the car’s parking permissions in a way that can be called back to.
The WKU Parking and Transportation Services team has a van with the antennae mounted on the sides, allowing for continuous scanning while driving through the parking zones.
Insert Image of
Parking Pass
The Alien P.R.O.B.E. app has multiple menu screens as pictured above, these allow the user to navigate to the section of the app with the functionality they need at that moment.
The Setup button opens the portion of the app that allows the user to determine what type of connection they will use as well as set it up. If the connection between the reader and the app is through a network connection, the user inputs the reader IP, port, as well as their credentials to ensure only people with the correct access can access the reader functions. If the user is using a Bluetooth connection, the reader IP and port aren’t needed but the username and password credentials are to maintain security.
The Scan button leads to the main function of the app, when the On/Off switch is toggled On and the scan button is pressed the RFID Reader will begin sending tags to the app through the connection type specified in the Setup section. This checks for duplicate tags automatically to avoid clutter, and pressing the Clear button removes all tags from the view. All unique tags scanned within a session are stored in the Saved Tags section, which can be viewed at any time by pressing the View Saved Tags button on the Scan menu.
The About page gives user a brief description and tutorial of how to operate the app, including setting up the connection to the reader, and how to properly scan tags. It also includes the credits for the app, listing all developers and designers for the app.
This project introduces a mobile application that utilizes RFID technology to optimize parking management at WKU Parking and Transportation Services (WKU PTS). The "Alien P.R.O.B.E." mobile application aims to automate parking verification processes, enhancing operational efficiency and user experience for WKU Parking and Transportation workers. Utilizing an Alien F800 RFID reader and ALR-8698 RFID antenna, the mobile app's backend system scans parking permits' RFID. tags. Our app will then cross-reference the RFID tags with WKU's servers to check permissions and verify the tags. Our goal for this app is to reduce manual verification time and address unauthorized parking issues that the WKU PTS employees' encounter. By automating these processes, the project will streamline operations and improve overall parking experiences for users and Transportation service employees. The primary audience comprises WKU parking management teams, with the Senior Information Technology Consultant at WKU Parking and Transportation Services as the client. This project employs a systematic approach, emphasizing clear documentation, client engagement, and RFID technology application. The development follows distinct phases aligned with a modified waterfall model, ensuring adaptability and continuous improvement. The system offers a scalable, secure, and efficient solution for parking resource management at WKU.
Abstract
Equipment
App
What is this Project?
Reader and Antenna Connection
Alien P.R.O.B.E. App